The USRP B210 Current Hardware Revision: 5
The schematics of the board can be visited here http://files.ettus.com/schematics/b200/b210.pdf

As characterized the most important components of the SDR are listed below
Part Number	Description	fabrication	thermal characterisation	radiation characterisation	TID	SEE	TID comment
Mini-Circuits TCM1-63AX+	Transformer		-40°C to 85°C
Analog Devices AD9361	RF Transceiver		-40°C to 85°C
Xilinx Spartan-6 XC6SLX150	FPGA	45 nm low-power copper process technology	** / -40°C to 100°C	up to 100krad			Ref 3 paragr.
ADF4001	Frequency Synthesizer		-40°C to 85°C
CYUSB3014	FX3: SuperSpeed USB Controller		-40°C to 85°C
EZ-USB FX3™ Product Page
SKY13317	Antenna Switch	a GaAs pHEMT single-pole	-40°C to 100°C
BD3150L50100A00	Balun	not even a contact point			immune?	immune?	99% sure. needs bibliography
PGA−102+	Amplifier	E-PHEMT technology	-40°C to 85°C
525L20DA40M0000	VCTCXO (B200/B210 only)	Fundamental Crystal Design	-40°C to 85°C		not immune	not immune	need to define the radiation tolerance bibliographically
Jackson Labs LC_XO Spec Sheet Manual	Optional GPSDO (B200/B210 only)	probably 3.3V cmos	-45°C to +85°C
resistors			most -40°C to 85°C	resistant enough in compare with other components on the board	immune	immune	according to REF 1 page 66(59)
capacitors			most -55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)			according to REF 1 page 66(59) / & Ref2 page 20
pcb

**

Ref 1 Nuclear radiation hardening for electronic components (LOCKHEED MISSILES & SPACE COMPANY August 1969)
Ref 2 Report on the Effect of Radiation on Resistors and Capacitors for the HV filter circuit of the Endcap VPT (By Ignacio Yaselli, 04/08/2004)
Ref 3 A Commercial 65 nm CMOS Technology for Space Applications: Heavy Ion, Proton and Gamma Test Results and Modeling