\
Supplier Part Number 1	Part Description	Fabrication	Thermal Characterization	Radiation Characterization	TID	SEE	TID comment
2332478RL	10pF ±5% 25V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
445-9066-1-ND	1µF ±10% 10V X5R Ceramic Capacitor -55°C ~ 85°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)		-55°C to 85°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-1024-1-ND	100pF ±5% 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
81-GRM155R71C104KA88	0.10µF ±10% 16V X7R Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)	Murata: Please contact us before using our products for the applications in Aerospace equipment	-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
490-6241-1-ND	47pF ±1% 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
490-3237-1-ND	510pF ±5% 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
587-5864-2-ND	1µF ±20% 6.3V X5R Ceramic Capacitor -55°C ~ 85°C Surface Mount, MLCC 0201 (0603 Metric) 0.024" L x 0.012" W (0.60mm x 0.30mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
445-7275-1-ND	1000pF ±10% 25V X7R Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0201 (0603 Metric) 0.024" L x 0.012" W (0.60mm x 0.30mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-1448-2-ND	10µF ±20% 6.3V X5R Ceramic Capacitor -55°C ~ 85°C Surface Mount, MLCC 0603 (1608 Metric) 0.063" L x 0.031" W (1.60mm x 0.80mm)		-55°C to 85°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
490-12232-1-ND	0.10µF ±10% 6.3V X6S Ceramic Capacitor -55°C ~ 105°C Surface Mount, MLCC 0201 (0603 Metric) 0.024" L x 0.012" W (0.60mm x 0.30mm)	Murata: Please contact us before using our products for the applications in Aerospace equipment	-55°C to 105°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
2332478RL	10pF ±5% 25V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune?	immune?	if it is critical we have to check it as it is in the area of <10pF
490-4516-2-ND	10000pF ±10% 50V Ceramic Capacitor X7R 0402 (1005 Metric) / Chip Monolithic Ceramic Capacitor	Murata: Please contact us before using our products for the applications in Aerospace equipment	-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-1706-1-ND	CAP CER 0.018UF 16V X7R 0402		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
490-6241-1-ND	47pF ±1% 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
490-5408-1-ND	4.7µF ±20% 6.3V X5R Ceramic Capacitor -55°C ~ 85°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)	Murata: Please contact us before using our products for the applications in Aerospace equipment		resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
490-7201-2-ND	10µF ±20% 16V X5R Ceramic Capacitor -55°C ~ 85°C Surface Mount, MLCC 0603 (1608 Metric) 0.063" L x 0.031" W (1.60mm x 0.80mm)			resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
810-C1608X5R1A226M	22µF ±20% 10V X5R Ceramic Capacitor -55°C ~ 85°C Surface Mount, MLCC 0603 (1608 Metric) 0.063" L x 0.031" W (1.60mm x 0.80mm)			resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
ESD8472MUT5GOSCT-ND	TVS DIODE 5.3VWM 14VC X3DFN2				immune?	immune?	99% sure. needs bibliography
ESD7016MUTAGOSDKR-ND	TVS DIODE 5VWM 10VC 8UDFN				immune?	immune?	99% sure. needs bibliography
259-1572-ND	FAN AXIAL 30X6.9MM 5VDC WIRE			resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	no worth for space application(heat is dissipated though attenuators
587-3277-1-ND	FERRITE BEAD 600 OHM 0201 1LN				immune?	immune?	99% sure. needs bibliography
445-9329-2-ND	FERRITE BEAD 220 OHM 0402 1LN				immune?	immune?	99% sure. needs bibliography
445-2206-2-ND	FERRITE BEAD 600 OHM 0805 1LN				immune?	immune?	99% sure. needs bibliography
LMS7002M	IC FPRF Transceiver LMS7002M; 261 pin aQFN	65nm CMOS	-40°C to 85°C		TID immune to 100 krad(Si) cumulative dose.		https://www.researchgate.net/publication/224168100_A_Commercial_65_nm_CMOS_Technology_for_Space_Applications_Heavy_Ion_Proton_and_Gamma_Test_Results_and_Modeling
497-15739-1-ND	EEPROM Memory IC 128Kb (16K x 8) I²C 1MHz 450ns 8-UFDFPN (2x3)	STMicroelectronics: we have asked over their webpage	-40°C to 85°C
863-1455-1-ND	RF Switch IC 802.11a/b/g/n DPDT 50 Ohm 6-MLPD (1.5x1.5)	skyworks: we have asked over their webpage	-40°C to 85°C
544-3110-ND	IC FPGA/CPLD NV 130 I/O 169UBGA	55 nm TSMC Embedded Flash (Flash + SRAM) process technology	0°C to 85°C (that is the commercial one there is also the industrial)		send but not yet
768-1311-ND	IC USB3-32BIT SYNC FIFO 76QFN	FTDI: we have sent email	-40°C to 85°C		NA they sent the document. no reference to the production technology
LMK00105SQ/NOPBCT-ND	IC CLK BUFFER 2:5 200MHZ 24WQFN	Ultra-Low Jitter LVCMOS	-40°C to 85°C
568-9815-2-ND	SENSOR TEMPERATURE I2C 8HWSON	NXP Semiconductors: we have asked over their webpage	-55°C to 125°C
296-24180-1-ND	8 Bit Digital to Analog Converter 1 SC-70-6	are fabricated using Texas Instruments' proprietary HPA07 process technology. (5V isolated CMOS transistors. 0.3 µm feature sizes)	-40°C to 125°C
W25Q40EWUXIE CT-ND	FLASH - NOR Memory IC 4Mb (512K x 8) SPI 8-USON (2x3)	?winbond: we have asked	-40°C to 85°C
1092-1123-ND	FLASH - NOR Memory IC 16Mb (2M x 8) SPI 104MHz 8-SOP	CMOS	-40°C to 85°C
490-7312-6-ND	DC/DC CONVERTER 3.6V 3A SMD	Murata: we have asked over their webpage	-40°C to 85°C
497-11013-1-ND	Linear Voltage Regulator IC Positive Adjustable Output 0.8 V ~ 4.5 V 1A 6-DFN (3x3)	PMOS?	-40°C to 125°C
CON-SMA-EDGE-S-ND	SMA Connector Jack, Female Socket Board Edge, End Launch Solder		?	NA	immune	immune	NA is mechanical part
S1012E-07-ND	7 Positions Header, Unshrouded, Breakaway Connector 0.100" (2.54mm) Through Hole Tin		-65°C to 125°C	NA	immune	immune	NA is mechanical part
952-1389-ND	CONN HDR 1.27MM SMD AU 10POS		-40°C to 105°C	NA	immune	immune	NA is mechanical part
952-1389-ND	CONN HDR 1.27MM SMD AU 10POS		-40°C to 105°C	NA	immune	immune	NA is mechanical part
609-4726-ND	5 Positions Header Connector 0.100" (2.54mm) Through Hole Tin		?	NA	immune	immune	NA is mechanical part
732-3157-ND	USB - A USB 3.0 (USB 3.1 Gen 1, Superspeed) Plug Connector 9 Position Surface Mount, Right Angle		-20°C to 85°C	NA	immune	immune	NA is mechanical part
WM5587CT-ND	Ultra Miniature Coaxial Connector Receptacle, Male Pin 50 Ohm Surface Mount Solder		-40°C to 90°C	NA	immune	immune	NA is mechanical part
3M9447-ND	2 Positions Header, Unshrouded Connector 0.100" (2.54mm) Through Hole Gold		-25°C to 105°C	NA	immune	immune	NA is mechanical part
516-1419-1-ND	LED GREEN/RED DIFFUSED 0603 SMD
859-LTST-S326KGJRKT	LED GREEN/RED CLEAR 2SMD R/A
2361677	RFI SHIELD CLIP MINI TIN SMD			NA	immune	immune	NA is mechanical part
1909662	Enclosure, Shielding Cabinet Cover, Shielding Cabinet, 25 mm, 25 mm, 3 mm, Tin Plate			NA	immune	immune	NA is mechanical part
TDYSFF-M3/5	Screwed spacer sleeve; Int.thread: M3; 5mm; brass			NA	immune	immune	NA is mechanical part
M3X3/D7985, M3X3/D7985, M3X8/D7985B, M3X8/D7985B	Screw; M3x3; DIN:7985; Head: cheese head; Phillips; steel; zinc; PH1, Screw; M3x3; DIN:7985; Head: cheese head; Phillips; steel; zinc; PH1, Screw; M3x8; DIN:7985; Head: cheese head; Phillips; black finish, Screw; M3x8; DIN:7985; Head: cheese head; Phillips; black finish			NA	immune	immune	NA is mechanical part
2285826	Surface Mount High Frequency Inductor, 0402HP Series, 8.2 nH, ± 5%, 0402 [1005 Metric], 5.4 GHz				immune?	immune?	99% sure. needs bibliography
490-6269-1-ND	0.80pF ±0.1pF 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)	Murata: Please contact us before using our products for the applications in Aerospace equipment		resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune?	immune?	if it is critical we have to check it as it is in the area of <1pF
445-4854-6-ND	1pF ±0.1pF 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)	TDK:Please contact us before using our products for the applications in Aerospace equipment		resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune?	immune?	if it is critical we have to check it as it is in the area of <1pF
311-1001-1-ND	0.50pF ±0.25pF 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)			resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune?	immune?	if it is critical we have to check it as it is in the area of <1pF
445-1071-1-ND	FIXED IND 100UH 2MA 3.1 OHM SMD	TDK:Please contact us before using our products for the applications in Aerospace equipment
311-0.0JRTR-ND	RES SMD 0.0OHM JUMPER 1/16W 0402			resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
2332536	SMD Multilayer Ceramic Capacitor, U Series, 2 pF, ± 0.1pF, C0G / NP0, 50 V, 0402 [1005 Metric]		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune?	immune?	if it is critical we have to check it as it is in the area of <1pF
490-5927-1-ND	'1.2pF ±0.25pF 50V C0G, NP0 Ceramic Capacitor -55°C ~ 125°C Surface Mount, MLCC 0402 (1005 Metric) 0.039" L x 0.020" W (1.00mm x 0.50mm)	Murata:Please contact us before using our products for the applications in Aerospace equipment	-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune?	immune?	if it is critical we have to check it as it is in the area of <1pF
445-1071-1-ND	FIXED IND 100UH 2MA 3.1 OHM SMD	TDK:Please contact us before using our products for the applications in Aerospace equipment	-55°C to 125°C		immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-10.0KLRTR-ND	RES SMD 10K OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
1276-3469-6-ND	RES SMD 49.9 OHM 1% 1/16W 0402		-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
RMCF0402FT2K20CT-ND	RES SMD 2.2K OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
541-560LCT-ND	RES SMD 560 OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
RMCF0402FT100RDKR-ND	RES SMD 100 OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-2.49KLRDKR-ND	RES SMD 2.49K OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
RMCF0402FT1K00TR-ND	RES SMD 1K OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-0.0MCT-ND	RES SMD 0.0OHM JUMPER 1/20W 0201	RC series chip resistors with lead free terminations made by thick film process	-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
P10.0ABCT-ND	RES SMD 10 OHM 1% 1/20W 0201	Thick Film Chip Resistors	-55°C to 125°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-4.7KLRCT-ND	±1% 0.063W, 1/16W Chip Resistor 0402 (1005 Metric) Moisture Resistant Thick Film	RC series chip resistors with lead free terminations made by thick film process	-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
YAG3045CT-ND	RES SMD 1.6K OHM 1% 1/16W 0402	RC series chip resistors with lead free terminations made by thick film process	-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-22.0LRTR-ND	RES SMD 22 OHM 1% 1/16W 0402	RC series chip resistors with lead free terminations made by thick film process	-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
RMCF0402FT3K00TR-ND	RES SMD 3K OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
RMCF0402FT3K83CT-ND	RES SMD 3.83K OHM 1% 1/16W 0402		-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
YAG3189CT-ND	RES SMD 576 OHM 1% 1/16W 0402	RC series chip resistors with lead free terminations made by thick film process.	-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-8.20KLRCT-ND	RES SMD 8.2K OHM 1% 1/16W 0402	RC series chip resistors with lead free terminations made by thick film process.	-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
311-15.0KLRCT-ND	RES SMD 15K OHM 1% 1/16W 0402	RC series chip resistors with lead free terminations made by thick film process.	-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
YAG3512CT-ND	±1% 0.063W, 1/16W Chip Resistor 0402 (1005 Metric) Automotive AEC-Q200, Moisture Resistant Thick Film	chip resistors with leadfree terminations made by thick film process.	-55°C to 155°C	resistant enough in compare with other components on the board (critical components for the functionality, should be checked again)	immune	immune	according to REF 1 page 66(59) / & Ref2 page 20
TC1-1-13M-45+	RF balun; 1:1 ratio; 3 dB bandwidth: 0.3 MHz to 3.5 GHz; 3.8mm x 3.8mm		-40°C to 150°C		immune?	immune?	99% sure. needs bibliography
568-12530-6-ND	RF MOSFET Transistors Trans MOSFET N-CH 7V 0.03A 4pin(3+Tab)	NMOS	x?- to 150°C
IRLML6244TRPBFTR-ND	N-Channel 20V 6.3A (Ta) 1.3W (Ta) Surface Mount Micro3™/SOT-23	NMOS	-55°C to 150°C
RTX5032A	RTX5032A 40MHz, High performance TCXO, With VC, Filter Enabled, 10-pin 5mm x 3.2 mm x 1.65 mm package	Rakon: we have asked over their webpage			not immune	not immune	need to define the radiation tolerance bibliographically
1253-1368-1-ND	30MHz ±10ppm Crystal 8pF 50 Ohm -40°C ~ 85°C Surface Mount 4-SMD, No Lead (DFN, LCC)	Kyocera International Inc: / we have asked over their webpage			not immune	not immune	need to define the radiation tolerance bibliographically

Ref 1 Nuclear radiation hardening for electronic components (LOCKHEED MISSILES & SPACE COMPANY August 1969)
Ref 2 Report on the Effect of Radiation on Resistors and Capacitors for the HV filter circuit of the Endcap VPT (By Ignacio Yaselli, 04/08/2004)
Ref 3 A Commercial 65 nm CMOS Technology for Space Applications: Heavy Ion, Proton and Gamma Test Results and Modeling